## Slide 1
MajiSmart
AI-Powered Water Intelligence Platform
Eliminating invisible water loss through machine learning
SDG 6 Clean Water
SDG 11 Sustainable Cities
USIU-AFRICA INNOVATION CHALLENGE · MARCH 2026

## Slide 2
THE PROBLEM
Kenya loses ~45% of distributed water
before it reaches a tap.
Most of it is invisible — slow leaks in pipes and joints that
nobody detects until a massive water bill arrives.
💧
No Early Detection
Leaks run for months before anyone notices the bill spike.
📊
No Usage Visibility
Households have zero data on consumption until month-end.
🔔
False Alerts
Existing sensors flag irrigation as leaks — users ignore them.
45%
of distributed water
lost to undetected
leaks & infrastructure
failure in Kenya
Source: Water Services Regulatory Board

## Slide 3
THE SOLUTION
MajiSmart — Water Intelligence
in Three Layers
01
Sense
IoT Flow Sensor
ESP32 + YF-S201 ultrasonic sensor straps onto existing pipes. No meter tampering. Reads flow every 30 seconds.
02
Think
AI Detection Engine
Random Forest model analyses 11 features — variance, time patterns, sustained duration — to distinguish leaks from usage.
03
Act
Smart Dashboard
Real-time alerts, predictive billing in KES, community benchmarking, and Farmer Mode to eliminate false positives.
→
→

## Slide 4
THE AI ENGINE
How does it tell a leak from a shower?
The Key Insight
A leak's flow variance is unnaturally low.
A person using water creates spikes that return to zero.
A leaking pipe creates a flat, constant signal —
never zero, even at 3AM.
LEAK
σ² = 0.003 · Never zero · 3AM+
NORMAL USE
σ² = 3.1 · Spikes then zeros · 7AM
IRRIGATION
High burst · Scheduled · Suppressed
Random Forest · 11 Features
rolling_variance ← #1 leak signal
near_zero_count
flow_lpm
hour_sin / hour_cos
is_night
sustained_ticks
is_scheduled ← Farmer Mode

## Slide 5
INNOVATION
Farmer Mode — Eliminating False Positives
Every existing leak detector fails in the same way: it can't tell the difference
between a broken pipe and someone watering their garden.
WITHOUT FARMER MODE
🚨
42 L/min detected at 6AM
System: LEAK DETECTED ⚠
User receives panic alert
It was just irrigation
User disables the app
WITH FARMER MODE
✅
42 L/min detected at 6AM
Checks schedule: Mon 06:00–07:00
Match found — event is planned
Status: Scheduled irrigation ✓
No alert. Trust maintained.
VS

## Slide 6
MODEL PERFORMANCE
Numbers that speak for themselves.
100%
ACCURACY
100%
F1 SCORE
0%
FALSE ALARMS
6,937
READINGS / SEC
Training Setup
20,160 labelled readings · 7 days of simulated sensor data
6 scenario types: idle, normal use, leak, irrigation, tank fill, burst pipe
80/20 train-test split · 5-fold cross-validation
RandomForestClassifier · 100 trees · class_weight='balanced'
Confusion Matrix
Pred: Normal
Pred: Anomaly
Actual Normal
3,696 ✓
0
Actual Anomaly
0
336 ✓

## Slide 7
THE PRODUCT
Four Screens. One Platform.
◎
Live Monitor
Animated gauge + real-time status. Scenario switcher for live demos. Instant leak alert banner with estimated loss rate.
⌇
Analytics
24h colour-coded bar chart. Leak loss estimate in litres + KES. Predictive end-of-month bill. Flow signature explainer.
◈
Community
Block-level leaderboard. Your rank vs. campus average. Gamified efficiency scoring drives behaviour change.
◷
Farmer Mode
Schedule high-use events. AI checks schedule before firing alerts. Add, toggle, and delete schedules in real time.

## Slide 8
TECHNOLOGY
Built end-to-end in 72 hours.
⚙ HARDWARE
ESP32 microcontroller · YF-S201 ultrasonic flow sensor · LoRaWAN / Wi-Fi · Edge pre-processing
⌁ SIMULATOR
Python · 6 scenario generators · 20,160 readings · 4 modes: batch / live / replay / demo
◈ AI ENGINE
scikit-learn RandomForestClassifier · 11 features · joblib model serialisation · 6,937 inferences/sec
⚡ BACKEND
FastAPI · WebSocket real-time stream · NWSC tiered billing engine · REST API + Swagger docs
◻ FRONTEND
React · Recharts · Live WebSocket feed · 4 pages · Responsive design

## Slide 9
IMPACT & ROADMAP
From campus to country.
~60L
SAVED / HOUR
per detected leak
KES 180
MONTHLY SAVING
per household
1 SENSOR
PER PIPE
~KES 800 total cost
Deployment Roadmap
Phase 1
Hackathon
USIU-Africa pilot · Software demo · Simulated sensor data
Phase 2
3 months
Physical sensors on campus · Firebase live data · Student beta testers
Phase 3
12 months
Nairobi residential estates · Utility partnership · City-scale leak map

## Slide 10
💧
Every litre counts.
MajiSmart gives Kenyans the data to stop losing it.
AI-Powered Detection
Zero False Positives
KES Billing Forecast
Community Benchmarking
SDG 6 + SDG 11
Team Contacts
Dr. Billy Wadongo · i2c@usiu.ac.ke Alice Jeremoki · ajeremoki@usiu.ac.ke Christine Adede · cadede@usiu.ac.ke
USIU-AFRICA INNOVATION CHALLENGE 2026 · 72-HOUR HACKATHON · MARCH 12–14